## Slide 1
Primary funding is provided by
The SPE Foundation through member donations
and a contribution from Offshore Europe
The Society is grateful to those companies that allow their professionals to serve as lecturers
Additional support provided by AIME
Society of Petroleum Engineers Distinguished Lecturer Program
www.spe.org/dl
Notes: AIME = American Institute of Mining, Metallurgical and Petroleum Engineers

## Slide 2
Society of Petroleum Engineers Distinguished Lecturer Program
www.spe.org/dl
John D. Macpherson
Automation of the Drilling System: What has been done, what is being done, and why it is important

## Slide 3: Presentation Outline
Definitions and background
The drivers for automation
Technical and Business Challenges
SPE Drilling Systems Automation TS
A brief look into automation systems
Conclusions
Q&A

## Slide 4: Drilling Systems Automation (DSA)
Involves the control of the drilling process by automatic means, ultimately reducing human intervention to a minimum.
Employs control systems and information technologies
Includes all components downhole, on surface and remote to the drilling rig that are used in real-time to drill the wellbore.

## Slide 5
The process of creating a borehole with systems and sub-systems that are computer controlled, leading to reduced human intervention
What is Drilling Systems Automation?
Remote
BHA
Rigsite
Enterprise
5
Notes: Current state-of-the-art is that we have isolated sites of automation: downhole in the MWD tools, on the surface at the rigsite, and remote in the data center. Each of these is discrete and is at a different level of automation. The objective of “Drilling Systems Automation” is to bridge these islands of drilling automation by creating an “automated drilling system” which delivers many productivity and safety benefits to all oilfield companies. There are many groups working to create the correct environment for drilling systems automation. But more about all this later, and let’s work on a few definitions first.

## Slide 6
Levels | Monitor |  | Advise |  | Select/Decide |  | Implement | 
Manual Control | H |  | H |  | H |  | H | 
Action Support | H | C | H |  | H |  | H | C
Batch Processing | H | C | H |  | H |  |  | C
Shared Control | H | C | H | C | H |  | H | C
Decision Support | H | C | H | C | H |  |  | C
Blended Decisions | H | C | H | C | H | C |  | C
Rigid System | H | C |  | C | H |  |  | C
Auto Decisions | H | C | H | C |  | C |  | C
Supervisory Ctrl | H | C |  | C |  | C |  | C
Full Automation |  | C |  | C |  | C |  | C
1
Levels of Computerization
Functions
H – Human C - Computer
Ref: Endsley and Kaber, 1999,
Ergonomics, Vol. 42
6
2
3
4
5
6
7
8
9
10
Notes: Endsley and Kaber define levels of automation by function: monitoring, advice generation, selecting (decision) and implementation (control). H corresponds to Human involvement in the function, while C corresponds to computer involvement. Note that each function, for example monitoring, is present over a wide range in levels of automation. However monitoring is the predominant computer function at lower levels of automation, and the progression is monitoring to advice to decision to control with increasing levels of automation.

## Slide 7
Control Systems on Offshore Rigs
Dynamic
Positioning
Power
Management
Thruster
Control
BOP Control
Hydraulic
Systems
Drillship: Pacific Drilling, Pacific Santa Ana
Active Heave
Drawworks
7

## Slide 8
Monitor
L2
Advise
L3-L4
Control
L5-L7
Drilling Dynamics Diagnostic Systems
Autonomous
L8-L10
Auto-Driller
Wellsite Monitoring Systems
MPD Control Systems
LWD Formation Samplers
Remote Data Centers
Directional Drilling Advisors
Smart Alarms
Stick-Slip Surface Control
MWD Rotary Steerable Systems
Drilling Systems Automation
The current level of automation in Drilling
Surface Digital Networks
MWD Network
10101011100100110001
Source: Macpherson etal, 2013, SPE 166263
8
Notes: The state of the art in drilling automation is actually quite impressive. For human and computer monitoring, both wellsite-based and remote systems are readily available, are quite advanced, and are being work on daily. For computer based advisory systems, a great deal of effort has been expended in interpreting data downhole and transmitting compressed diagnostics to surface. Directional drilling advisors (geosteering for example) are often executed remotely or at the wellsite, and control systems (auto-drillers are one example) are present at the wellsite. However, the highest degree of automation are downhole autonomous or semi-autonomous drilling systems, such as RSS, which compare favorably with anything developed in any industry, especially considering their operating environment.
The high degree of downhole automation is needed because there is (has been) a digital restriction between downhole and surface.

## Slide 9: Drilling Systems Automation
The drilling industry has equipment that is highly automated (level 8+)
Automation of drilling systems and processes is quite rudimentary (level 3)
Why?
What are the business drivers?

## Slide 10
Well Complexity
Difficult profiles, bottomhole pressure margins
NPT
Significant
35 to 40% of deep-water drilling costs
Minimized by responding predictably to events
Well Manufacturing
Drill many similar profile wells per field
Repetitively drill to plan with minimal risk and cost
Mitigate risk and control costs
Data
Overload
Real-time measurements, complex operations
Manage, interpret, act on large volumes of data
DSA Drivers
10
Source: Baker Hughes

## Slide 11
Well Complexity
Difficult profiles, bottomhole pressure margins
NPT
Significant
35 to 40% of deep-water drilling costs
Minimized by responding predictably to events
Well Manufacturing
Drill many similar profile wells per field
Repetitively drill to plan with minimal risk and cost
Mitigate risk and control costs
Data
Overload
Real-time measurements, complex operations
Manage, interpret, act on large volumes of data
DSA Drivers
11
Don’t buckle the pipe
Don’t exceed the maximum RPM of the bit
Stay on target
Don’t exceed maximum weight on the bit
Drill efficiently
Avoid lateral vibrations
Avoid stick-slip vibrations
Don’t exceed make-up torque of the drill string
Don’t stall the downhole motor
Don’t stall the top drive
Drill faster
Don’t exceed the maximum RPM of the top drive
Connect a new pipe joint fast and safely
Condition
the hole
Go back to bottom fast and safely
Clean the hole
Drill this section without tripping; i.e. with one bit
Time is money
Safety first
Source: Mark Anderson, Shell

## Slide 12
Well Complexity
Difficult profiles, bottomhole pressure margins
NPT
Significant
35 to 40% of deep-water drilling costs
Minimized by responding predictably to events
Well Manufacturing
Drill many similar profile wells per field
Repetitively drill to plan with minimal risk and cost
Mitigate risk and control costs
Data
Overload
Real-time measurements, complex operations
Manage, interpret, act on large volumes of data
DSA Drivers
12

## Slide 13
Well Complexity
Difficult profiles, bottomhole pressure margins
NPT
Significant
35 to 40% of deep-water drilling costs
Minimized by responding predictably to events
Well Manufacturing
Drill many similar profile wells per field
Repetitively drill to plan with minimal risk and cost
Mitigate risk and control costs
Data
Overload
Real-time measurements, complex operations
Manage, interpret, act on large volumes of data
DSA Drivers
13
Source: SPE 178875, 2016, Livingston etal, Team Approach to Horizontal Drilling Optimization in the Marcellus Delivers Record Setting Performance

## Slide 14
Well Complexity
Difficult profiles, bottomhole pressure margins
NPT
Significant
35 to 40% of deep-water drilling costs
Minimized by responding predictably to events
Well Manufacturing
Drill many similar profile wells per field
Repetitively drill to plan with minimal risk and cost
Mitigate risk and control costs
Data
Overload
Real-time measurements, complex operations
Manage, interpret, act on large volumes of data
DSA Drivers
14

## Slide 15
Expert Resources
Operations starved for expertise
Skilled employees exiting the industry
HS & E
Driver is to make the work environment a safer place
Reduce the number of people in “red zones.”
Knowledge Transfer
Will make available scarce expert resources
Transfer knowledge from skilled to new employees
DSA Drivers
15

## Slide 16: Technology and Business
There are significant business drivers behind drilling systems automation
But to make DSA happen we have to communicate the technology to the business

## Slide 17
Technology: DSA is Challenging
Necessity of domain expertise in technology enablers
Task uncertainty
Source: UT Austin RAPID Consortium

## Slide 18: DSA Decision Making and Control Framework
Execution
Machine Control
Machine Control Systems
Well
Construction
Physical Drilling Process
Operations
Enterprise
Wellsite & Remote Operations
Well Design, Budget, Data Repository,
Data mining & analytics
Monitoring, Modeling, Simulation
Process Control Systems
Onsite Interpretation & Control
Instrumentation & Measurement
No Intelligent Sensing
0
1
2
3
4
Modified from ISA 95 for the Drilling Process
Source: de Wardt etal, 2015, SPE 173010
Wellsite
Remote
OPC UA
Deterministic Protocol
WITSML
Non-deterministic Protocol

## Slide 19: DSATS Rig Control System
SPE Drilling Systems Automation Technical Section
Operators,
Service
Companies,
Drilling
Contractors,
Equipment
Suppliers,
…

## Slide 20: DSATS Communications Guidelines
OPC UA protocol for automation communications
Interface to proprietary or other standards
Machine independent software
  data-to-information
  control algorithms
Standardized method for real-time drilling data
Simplified device control architecture for drilling rigs
Standardized units, security, rig-information-model
Next Step: Data

## Slide 21: DSA Decision Making and Control Framework
Execution
Machine Control
Machine Control Systems
Well
Construction
Physical Drilling Process
Operations
Enterprise
Wellsite & Remote Operations
Well Design, Budget, Data Repository,
Data mining & analytics
Monitoring, Modeling, Simulation
Process Control Systems
Onsite Interpretation & Control
Instrumentation & Measurement
No Intelligent Sensing
0
1
2
3
4
Data Mining
Analytics
Subsurface
Predictions
Swab Surge ROP
Machine Control
Data flow between levels of the framework (NO SILOS)

## Slide 22: Data in Systems Automation
Without data there is no automation
“First comes data” (Lord Kelvin)
Who owns the data?
  Separation of Ownership and Confidentiality
  Data Silos versus Open System
  Embedded in the business model

## Slide 23
Sensors
& IMS
Communications
Machines Equipment
Control Systems
Simulation & Modeling
Human Factors
Certification & Standards
Data Aggregator
telemetry, latency
accuracy, precision
Completeness
Logic
Proximity
Accuracy
Conversion
Criticality
Availability
Data, Derived Data, System State
Calibration
Validity
data
Instrumentation and Measurement System (IMS) -centric view of drilling systems automation, showing relationship with other challenges
2
3
4
5
6
7
8
Systems Architecture
1

## Slide 24: Data Flow and Value
0
1
2
3
4
Well
Construction
Machine Control
Execution
Operations
Enterprise
REAL-TIME
SENSOR
DATA
IN STREAM
ANALYTICS
ENTERPRISE MODELING
ACTIVE
ADVISORY
PERFORMANCE
VISUALIZATION
CONTROL
Source: DSATS Luncheon Presentation, 2015, SPE Digital Energy Conference

## Slide 25: Data Flow and Value
Level 0:Physical process
Level 1: Machine Control
Level 2: Execution
HUMAN
COMPUTER
Source: Iversen et al., 2016 SPE-181047-MS

## Slide 26: A Brief Look into Systems
Control Loops
Concept: Drilling Control System
Implementation: Real-Time Data Modeling
Implementation: Wired Pipe and DSA

## Slide 27
Control Loops:
Flight Trajectory Control
Source: SPE-173396 • Automated Slide Drilling System and Multi-Body Dynamics Aided Slide Drilling Simulation • Ningyu Wang
Pilot
Pilot
Servo System
Attitude
Needed
Rudder Action
Needed
Rudder
Action
1
Notes: This is the plane control loop. The three control loops are now automated in onboard computers.
Manuscript: The flight trajectory is usually pre-designed by the airline company or the pilot. During the flight, the pilot modifies the target flight trajectory according to the real-time flight state, which includes the plane position and the wind velocity, etc. Based on the preset trajectory, the pilot figures out the plane’s target attitude, which is the work of the flight trajectory control loop. Should the plane roll to perform a coordinated turn? Or should it pitch the nose up for a climb? The planned plane attitude is realized by the actions of the plane’s rudders, and the plane attitude control loop calculates the needed rudder action. The rudder action commands are then executed by the motors and actuators, which makes the rudder control loop. The rudder actions directly change the aerodynamic shape of the plane and changes the aerodynamic load on the plane. The onboard sensors measure the plane’s position and attitude, and report to the pilot. All these three control loops can be realized in a set of onboard computers to replace the pilot and take over the plane control. The pilots in modern commercial flights can just sit and supervise the autopilot do its job

## Slide 28
Control Loops:
Well Trajectory Control
Directional
Driller
Driller
Servo
System
Drilling State
Needed
Actuator Action
Needed
Actuator
Action
Source: SPE-173396 • Automated Slide Drilling System and Multi-Body Dynamics Aided Slide Drilling Simulation • Ningyu Wang
1
Notes: Here we can decompose the drilling system.
In the third loop, the top drive and drawworks control are now automated.
The first two loops are under investigation.

## Slide 29: Drilling Control System
Source: Dashevskiy etal, 2003, AADE-03-NTCE-10
2

## Slide 30: Drilling Control System
Source: Dashevskiy etal, 2003, AADE-03-NTCE-10
End of training set
2

## Slide 31
Source: Chmela et al, 2014, SPE 168018
Model more accurate over time
Model data and sensor data deviate indicating a problem
Modeling for DSA
Use of mechanical, hydraulic and thermal models, in real-time, to derive “virtual sensor data”
3

## Slide 32: Modeling for DSA
Example, models predict safe “pull-window” during tripping
Set-points and operational constraints for safe, efficient operations
Staged introduction: monitoring, shadow system, then control
Source: Chmela et al, 2014, SPE 168018
3

## Slide 33
Automated Tripping System
Modeling for DSA
ECD
ECD
DEPTH (m)
DEPTH (m)
CSG SHOE DEPTH
CSG SHOE DEPTH
BITDEPTH
BITDEPTH
Pore Pressure
Pore Pressure
Manual System
Automated System
System automatically adjusts running speed and acceleration to avoid swab
Source: Chmela, etal. 2014, SPE 168018
3

## Slide 34
Surface Equipment
Wired Tubulars
Network Repeaters
Interface to MWD/LWD
Data Rate: 57kbps, low latency
Wired pipe and DSA
Source: Pixton and Craig, 2014, IADC/SPE 167965
4

## Slide 35
Drill String Telemetry
Controller
Dynamic Annular Pressure Control
Measurement While Drilling Surface System
Surface Data Logger
Wired pipe Systems
MWD
Hydraulic
Model
PLC
Wired pipe and DSA
Source: Fredericks etal, 2008, IADC/SPE 112651
Drilling shallow gas sands, offshore
MPD with wired pipe and downhole pressure measurements
4

## Slide 36
Connection BHP +/-45psi
Drilling
BHP +/-15psi
Connections
Casing Shoe pressure
Backpressure
Wired pipe and DSA
Source: Fredericks etal, 2008, IADC/SPE 112651
Bottom Hole and Casing Shoe Pressure (psi)
Bottom Hole Pressure from MWD
4

## Slide 37: Summary
Drilling Systems Automation (DSA)
  The process of creating a borehole with systems and sub-systems,
  That are computer controlled, and which
  Lead to reduced human intervention
Impact is across the entire organization and drilling process: Drill Bit to Enterprise

## Slide 38: Conclusions
While drilling equipment is highly automated, the drilling system/process is poorly automated.
Drilling systems automation is technically challenging, requires a holistic approach, and is rewarding with significant business drivers:
Performance, Safety and Cost

## Slide 39: Further Reading
SPE 166263, “Drilling Systems Automation: Current State, Initiatives and Potential Impact”, SPE ATCE, October 2013
SPE 173010, “Drilling Systems Automation Roadmap - The Means to Accelerate Adoption”, SPE/IADC Drilling Conference, London, March 2015

## Slide 40
Drilling Systems Automation Sources of Information
40
connect.spe.org/dsats/home/
connect.spe.org/dsaroadmap/home/
www.iadc.org/dsaroadmap
www.iadc.org/advanced-rig-technology-
committee/#access

## Slide 41
Society of Petroleum Engineers Distinguished Lecturer Program
www.spe.org/dl
41
Your Feedback is Important
Enter your section in the DL Evaluation Contest by completing the evaluation form for this presentation
Visit SPE.org/dl

## Slide 42: Data Flow and Value
Source: DSATS: Drilling Systems Automation Luncheon Presentation, Digital Energy Conference, The Woodlands, Texas, March 2015

## Slide 43: (5) Stick-Slip and ROP OPT

## Slide 44
Remote
Visualization
OPC UA
Tool
Comm App
OPC UA
App 3
OPC UA
App 2
OPC UA
[1] Drilling Automation System
OPC UA
System Processing
Planning, Reporting & Visualization
App 1
OPC UA
OPC UA Aggregation Server
OPC UA
MWD / Surface Logging
Surface Instrumentation
OPC UA
OPC UA
Drilling Rig
OPC UA
W.I.T.S.
Modbus
TCP
Gateway
WITSML

## Slide 45
Control
Wellsite Control Systems
Acquisition
Measurement Systems
Process
Physical Drilling Process
Remote
Enterprise
Monitoring, Modeling, Simulation
Database, Analytics
0
1
2
3
4
Standardized Communications – the enabler
OPC UA
WITSML
ISA-95 Automation Model

## Slide 46: Ex 3: Wired pipe and DSA
Source: Shishavan, etal., 2014, Multivariate Control for Managed Pressure Drilling Systems Using High Speed Telemetry, SPE 170962
Wired pipe with along-string sensors and real-time modeling for drilling control.