## Slide 1
Primary funding is provided by
The SPE Foundation through member donations
and a contribution from Offshore Europe
The Society is grateful to those companies that allow their professionals to serve as lecturers
Additional support provided by AIME
Society of Petroleum Engineers Distinguished Lecturer Program
www.spe.org/dl

## Slide 2
Society of Petroleum Engineers Distinguished Lecturer Program
www.spe.org/dl
Barbara G. Kutchko, PhD
US Department of Energy
National Energy Technology Laboratory
The New Science Behind Foamed Cement

## Slide 3: Agenda
Background
  What is foamed
  Why and where is it used?
  Key Issues
Project Description and Objectives
Laboratory Sampling Program & Analysis
Field Sampling Program & Analysis
Summary and Conclusions
Acknowledgements

## Slide 4: What is Foamed Cement?
Mixture of cement, foaming agents
and N2 gas
  Bubble Size Distribution (BSD) – small, evenly distributed, unconnected
Ultra low-density (lightweight)
Unique resistance to temperature & pressure-induced stresses
Minimal shrinkage
Provides superior gas migration protection
Much is assumed about field-generated properties

## Slide 5: Where is Foamed Cement Used?
Foamed cement is used globally (onshore and offshore)
  Middle East, South America, China, Africa, etc.
Typically used in:
  Weak formations with shallow flow risk
    Gulf of Mexico
    Fragile formations in California
    Weak/depleted zones in South Texas
  Steam Injection Wells
  Geothermal Wells
  Shale Gas Wells

## Slide 6: Key Issues
Laboratory test defined in American Petroleum Institute’s Recommended Practice (API RP) 10B-4 - Preparation and testing of Foamed Cement Slurries at Atmospheric Pressure (ISO 10426-4)
  Very little testing done above atmospheric pressure
Industry standards for lab testing not always realistic
  “Experts said that such tests were not foolproof ....” New York Times Nitrogen-Cement Mix Is Focus of Gulf Inquiry, 2010
After The Deepwater Horizon, Macondo Well incident, Foamed Cement was under multiple investigations and inquiries:
  United States Congressional Inquiries
  United States Department of Interior (DOI) – United States Coast Guard (USCG) Joint Commission
  National Academy of Engineering and National Research Council
  Service Companies and Operators – significant uncertainty
  API Cement Subcommittee 10C formed the Foamed Cement Work Group to address testing uncertainty

## Slide 7: Foamed Cement Research Scope
Project Description
Joint effort between API Sub-Committee 10 and NETL to examine foamed cement generated with lab equipment and field foamed cementing equipment
Research Questions
What parameters determine BSD (Bubble Size Distribution)?
  Pressure? Energy? Geometries of equipment?
How does BSD impact mechanical behaviors?
Is the API RP lab test adequate? Does it need to be improved?
Approach
Capture representative sets of foamed cement samples generated with both field and laboratory equipment

## Slide 8
Current Research Scope

## Slide 9: Lab vs Field
Air
Cement
Air + Cement
Nitrogen gas
Cement Slurry
Choke
Foamed Cement
API 10B-4 RP Multiblade Blender
High Pressure N2 Injection

## Slide 10: Atmospheric (blender) Foamed Cement
10%
170,000 individual bubbles identified in 1 cm3 subsample
20%
30%
Comparison of CT-derived entrained air fraction and foam quality denoting linear relationship
Details available in SPE-170298-MS, OTC-25776-MS

## Slide 11: Atmospheric (blender) Foamed Cement
Cores are approx ¼ inch in diameter
Resolution is approx 3.7 microns
Details available in SPE-170298-MS, OTC-25776-MS
FCR = Foamed Cement Recipe
10%
30%
40%
20%

## Slide 12: Atmospheric (blender) Foamed Cement
Cores are approx ¼ inch in diameter
Resolution is approx 3.7 microns
Details available in SPE-170298-MS, OTC-25776-MS
10%
30%
40%
20%
Chart: Young's Modulus vs. Entrained Air
| 0.1 | 0.2 | 0.3 | 0.4
FCR1 | 748178 | 585961 | 436483 | 310089
FCR2 | 520177.75 | 463177.6875 | 432481.8594 | 431481.5742
Chart: Strength vs. Entrained Air
| 0.1 | 0.2 | 0.3 | 0.4
FCR1 | 4303 | 3459 | 2211 | 1284
FCR2 | 4405 | 3607 | 2717 | 1617
FCR = Foamed Cement Recipe

## Slide 13: Field Generated Foamed Cement
3 field collections performed by 3 service companies with support from all the sponsors of the project
Field samples generated at elevated pressures ~300 to 1000 psi (2.1 to 6.9 MPa)
  Pump Rates: 3 – 5 BPM
Used identical equipment as full scale well cementing operation
Sampled with industry grade containers:
  Constant pressure (CP) vessels
  Aluminum (Al)-type, < 600-psi
  Stainless steel (SS), < 1,100-psi
  Dimensions: 3 ft. tall by 2 in diameter
Al
SS
CP Vessels
Details available in SPE-170298-MS, OTC-25776-MS

## Slide 14: Field Collection #1
Static - contained within 60 ft. of treating iron at target foamed quality and pressure
Cryogenic Liquid N2 Conversion to Gas N2
Sample pressure and foam quality targeted before collecting sample
Difficult to reach target pressure and quality
Details available in SPE-170298-MS, SPE-180333-MS

## Slide 15: Field Collection #2
Sample cylinder transport crate
Nitrogen Cooling Down
Dynamic - samples captured from live stream
Cryogenic Liquid N2 Conversion to Gaseous N2
No reduction in sample pressure and increase in sample nitrogen fraction due to loss of volume from sample lines
Pressure fluctuations caused multiple burst disk activations
Details available in OTC-25994-MS, SPE-180333-MS

## Slide 16: Field Collection #3
Base slurry mixing system
Bottled N2 source
CP Cylinders
Static - contained within treating iron at target foamed quality and pressure
Bottled N2 Gas through regulated flow
Pressure control throughout collection process with use of N2 bottle reservoir accumulator
Details available in SPE-180337-MS, SPE-180278-MS

## Slide 17: Field Generated Foamed Cement
Three dimensional (3-D) reconstruction of computed tomography scans of a pressurized field foamed cement

## Slide 18: Field Collection – CT Scans
Low High
CT Attenuation
FC1 41.2% 310 psi
Details available in SPE-170298-MS, SPE-180333-MS, SPE-180337-MS, SPE-180278-MS, OTC-25994-MS
Reconstructed medical CT images,
False color montage of 5 cross sections X-Z plane
FC2 27.9%
401 psi
2 in
FC3 8.3% 505 psi

## Slide 19: Structuring BSD
Real Bubble Suspensions (~30% Quality)
0
11
Bubble Radius
Bubble Size Comparison
Structuring Comparison
Similar Size Bubbles
3
38
Neighbors
Notes: LEFT: The bubbles are color coded by their radius. RIGHT: The bubbles are color coded by the number of nearest neighbors – an indication of structuring. Finding the nearest neighbors is a quick and easy method to process large data sets (shown here are the smaller data sets used for testing – in the much larger data sets that will be used in publications, we need something that can process large amounts of data). We have a collaboration with another professor at CMU to study these structures (future work).

## Slide 20: Summary and Conclusions
Field-generated: smaller bubble size, lower permeability, and increased strength
  Observed a strong relationship between the distribution of the bubbles and flow of the cement slurry
  Observed a strong relationship between the size of the bubbles and curing pressure
Properly-executed foamed cementing methods examined during this project all provided better material properties than previously thought
If an atmospherically-generated foamed cement sample exhibits acceptable foam stability, a foamed cement slurry of the same design and nitrogen fraction will be acceptable for use in well cementing operations.
January 2015

## Slide 21
Society of Petroleum Engineers Distinguished Lecturer Program
www.spe.org/dl
21
Your Feedback is Important
Enter your section in the DL Evaluation Contest by completing the evaluation form for this presentation
Visit SPE.org/dl

## Slide 22
Acknowledgements / Thank You / Questions
This work was completed as part of National Energy Technology Laboratory (NETL) research for the U.S. Department of Energy’s Complementary Research Program under Section 999 of the Energy Policy Act of 2005.
A special acknowledgement to Roy Long (NETL Strategic Center for Natural Gas and Oil) and Elena Melchert (DOE Office of Fossil Energy) for programmatic guidance, direction, and support.

## Slide 23
NETL Project Team Members
James Heathman, Shell
Glen Benge, Benge Consulting
Erick Cunningham, BP
Gunnar DeBruijn, Schlumberger
Joe Shine, Saudi Aramco (formerly of Baker Hughes)
Charles Buford, Profrac Services (formerly of Baker Hughes)
Craig Gardner, Chevron
Joe Maxson, Halliburton
Maggie Benge, Halliburton
Don “Woody” Lawrence, Sanjel International Saudi Arabia Ltd (formerly of BP)
API Foamed Cement Work Group
API Cement Subcommittee 10C
Dr. Barbara Kutchko
Dr. Dustin Crandall
Dr. Igor Haljasmaa
Johnathan Moore
Magdalena Gill
Richard Spaulding
Connor Gieger
Eilis Rosenbaum
Laura Dalton
Mary Tkach
Alison Mergaman
Jim Fazio
Bryan Tennant
Dr. William Harbert (University of Pittsburgh)
Dr. Tyler Ley (Oklahoma State University)
Dr. Kaushik Dayal (Carnegie Mellon University)
Industry Team Members

## Slide 24: Future Work
Further work to evaluate and implement improved laboratory methods to generate foamed cement under pressure, or with greater shear rate, could improve the correlation between current API laboratory test methods and foamed cements generated with field cementing equipment.
Look at longer term (lifetime) implications on cement integrity
Look at impact of temperature variations and flow
Develop an understanding of the thermodynamic processes involved (current PhD student working on this at CMU)

## Slide 25: Proof of Experimental Methodology Confirmed
Stability of the cement can be observed in both the CT images and physical measurements
Increasing the foam quality (gas fraction) increases the interconnectivity of the bubbles (visually) and the permeability (measured)
10 and 20% foam quality samples permeability did not appreciably change.
  Foam qualities of 10 and 20% achieve decreased slurry density without significantly increasing permeability.
Increasing the foam quality lowered Young’s modulus and compressive strength values
  Upper/lower boundary identified

## Slide 26
API Foamed Cement Working Group
Dedicated foam and cementing crew, cementing technical specialist, yard time and space to perform the sample collection
  Monitoring & measuring devices, liquid N2 tank, N2 conversion pump, foam injection pump, foam generator, cement mixing and pumping skid, bulk plant, tanks, hoses, iron
Liquid N2, water, API Class H cement, foaming agent and stabilizer
Additional iron and sensors required to construct the sampling manifold
Tank for disposal of slurry
Specially designed CT-transparent pressure vessels

## Slide 27
Field Collection # | Nitrogen Supply Method | Slurry state during collection | Pump Rates/Pressure Range | Strengths | Weaknesses
FC #1 | Cryogenic Liquid N2 Conversion to Gaseous N2 | Static – contained within treating iron at target foamed quality and pressure | 3 – 5 bpm 300 – 1000 psi | Sample pressure and foam quality could be targeted before trapping target sample | Difficult to reach target pressure and quality Loss of sample pressure due to volume loss
FC #2 | Cryogenic Liquid N2 Conversion to Gaseous N2 | Dynamic – samples captured from live stream pressure maintained through back pressure | 3 – 5 bpm 300 – 1000 psi | No reduction in sample pressure and increase in sample nitrogen fraction due to loss of volume from sample lines | Pressure fluctuations during test caused multiple burst disk activations
FC #3 | Bottled N2 Gas through regulated flow | Static – contained within treating iron at target foamed quality and pressure | 3 – 5 bpm 300 – 1000 psi | Pressure control throughout collection process with use of N2 bottle reservoir accumulator No requirement for N2 liquid to gas conversion provided reduced operational complexity and risks | 
NOTE: All tests conducted using API Class H cement mixed at 16.45 lb/gal base density

## Slide 28: Field Collection #1
Pressure Relief Valve
Pressure Transducers Connected to data recording system
Sample cylinder isolation valves. 2x2 lo-torque valve
Pressurized Sample Containers
To De-foaming Manifold
From Foamer Cross/Foam Generator
Sample isolation section. 38 ft of 2” treating line between 2x2 valves
Main treating line
Sample isolation valves. 2x2 lo-torque

## Slide 29: FINDINGS – Field Collection #1
Low High
CT Attenuation
YT1-D1 41.2% 310 psi
YT1-E1 33.6%
290 psi
YT1-D2 47.8% 290 psi
Details available in SPE-170298-MS, SPE-180333-MS
Reconstructed medical CT images,
False color montage of 5 cross sections X-Z plane
YT1-A1 30.1% 940 psi
Notes: Unlike the higher resolution industrial CT scans of atmospherically generated foamed cement (Kutchko et al 2013, Figure 9) the distribution of CTN from the medical CT scans is not bimodal with obvious CTN values for gas and cement. The majority of the bubbles within the foamed cement are below the voxel resolution of the medical scanner, causing a decrease in localized
Even though sample D2 is more uniform than sample D2 there is a distinct distribution of low density zones throughout the vessel. Visual examination of these slices indicate that there are fewer distinct low density structures within this sample, as compared to sample D1
Pressurized aluminum sample E1 was scanned and XZ montages of this vessel are shown in Figure CT11.This sample is distinctly different than the other three samples.

## Slide 30: FINDINGS – Field Collection #1
Chart: Porosity of CP Cylinder A1
| 47.1 | 46.6 | 49.2 | 49.2 | 47.7 | 47.7 | 49.9
Porosity | 544.285 | 494.41 | 456.56 | 400.04 | 333.495 | 265.82 | 190.77 | 116.81
Porosity | 544.285 | 494.41 | 456.56 | 400.04 | 333.495 | 265.82 | 190.77 | 116.81
Chart: Permeability of CP Cylinder A1
| 0.21 | 0.34 | 1.52 | 1.3 | 1.5 | 1.52 | 0.93
Permeability (mD) | 544.285 | 494.41 | 456.56 | 400.04 | 333.495 | 265.82 | 190.77 | 116.81
Chart: Porosity of CP Cylinder D1
| 38 | 33.299999999999997 | 39 | 40.6 | 40 | 40.700000000000003 | 39.5 | 41.6
Porosity | 544.285 | 494.41 | 456.56 | 400.04 | 333.495 | 265.82 | 190.77 | 116.81
Chart: Porosity of CP Cylinder D2
| 43.83 | 42.42 | 43.29 | 42.47 | 42.94
Porosity | 544.285 | 494.41 | 456.56 | 400.04 | 333.495 | 265.82 | 190.77 | 116.81
Chart: Permeability of CP Cylinder D2
| 0.51759999999999995 | 0.34870000000000001 | 0.31659999999999999 | 0.18579999999999999 | 0.19450000000000001
Permeability (mD) | 544.285 | 494.41 | 456.56 | 400.04 | 333.495 | 265.82 | 190.77 | 116.81
Chart: Permeability of CP Cylinder D1
| 0.11 | 0.03 | 0.36 | 0.28999999999999998 | 0.21 | 0.25 | 0.55000000000000004 | 0.28000000000000003
Permeability (mD) | 544.285 | 494.41 | 456.56 | 400.04 | 333.495 | 265.82 | 190.77 | 116.81
Chart: Porosity of CP Cylinder E1
| 31.4 | 34.200000000000003 | 34.5 | 33.200000000000003 | 34.4 | 35 | 29.2
Porosity | 544.285 | 494.41 | 456.56 | 400.04 | 333.495 | 265.82 | 190.77 | 116.81
Chart: Permeability of CP Cylinder E1
| 0.03 | 0.06 | 0.11 | 0.2 | 0.2 | 0.04 | 0.01
Permeability (mD) | 544.285 | 494.41 | 456.56 | 400.04 | 333.495 | 265.82 | 190.77 | 116.81
Details available in SPE-170298-MS, SPE-180333-MS
FC1-D1 41.2% 310 psi
FC1-E1 33.6%
290 psi
FC1-D2 47.8% 290 psi
FC1-A1 30.1% 940 psi

## Slide 31: Field Collection #2
Dual skid cement unit
Bulk cement
100 bbl Batch Mixer
Foam Manifold
N2 Unit
Data cabin
Waste Tank
Details available in OTC-25994-MS, SPE-180333-MS

## Slide 32: FINDINGS – Field Collection #2
2YT-A1 44.2% 490 psi
YT2-A4 27.9%
401 psi
YT2-A3 31.6% 363 psi
2 in
Reconstructed medical CT images,
False color montage of 5 cross sections X-Z plane
Details available in OTC-25994-MS, SPE-180333-MS
Low High
CT Attenuation
Notes: Captured under real-time conditions:
  Dynamic state, “on-the-fly”
  Pressures from 300 to 1,000-psi
  Rates from 1.8 to 6.5 bpm
  Full scale field service operation

## Slide 33: FINDINGS – Field Collection #2
Chart: Porosity of CP Cylinder A1
| 54.29 | 54 | 53.37 | 53.62 | 54.09 | 53.48 | 53.27 | 53.07 | 53.41 | 51.76
A1 | 434.19 | 383.34 | 349.55 | 318.74 | 288.83 | 252.8 | 212.37 | 186.47 | 119.42 | 76.51
Chart: Permeability of CP Cylinder A1
| 4.5030000000000001 | 4.2969999999999997 | 3.0310000000000001 | 3.512 | 5.4260000000000002 | 24.664000000000001 | 20.007999999999999 | 18.526 | 14.403 | 16.077999999999999
 | 434.19 | 383.34 | 349.55 | 318.74 | 288.83 | 252.8 | 212.37 | 186.47 | 119.42 | 76.51
Chart: Porosity of CP Cylinder A3
| 58.56 | 54.83 | 53.76 | 53.39 | 54.08 | 53.69 | 52.72 | 52.78 | 49.86
A3 | 462.87 | 394.2 | 323.96 | 284.24 | 262.15 | 231.83 | 120.91 | 94.16 | 52.04
Chart: Permeability of CP Cylinder A3
| 122.8 | 64.34 | 32.868000000000002 | 19.817 | 16.734999999999999 | 12.702 | 12.464 | 10.971 | 9.2810000000000006
A3 | 462.87 | 394.2 | 323.96 | 284.24 | 262.15 | 231.83 | 120.91 | 94.16 | 52.04
Chart: Porosity of CP Cylinder A4
| 45.15 | 38.909999999999997 | 41.73 | 41.42 | 42.2 | 41.05 | 40.840000000000003 | 30.4
A4 | 458.18 | 291.22 | 246.25 | 157.88 | 120.47 | 81.44 | 53.37 | 20.22
Chart: Permeability of CP Cylinder A4
| 0.22750000000000001 | 3.7100000000000001E-2 | 3.09E-2 | 6.2199999999999998E-2 | 4.3200000000000002E-2 | 0.19370000000000001 | 2.53E-2 | 0.1227
A4 | 458.18 | 291.22 | 246.25 | 157.88 | 120.47 | 81.44 | 53.37 | 20.22
Chart: Porosity of CP Cylinder SS1
| 53.56 | 51.99 | 51.09 | 43.54 | 37.56 | 34.31
SS1 | 450 | 365.4 | 332.3 | 263.93 | 191.88 | 122.87 | 49.6
Chart: Permeability of CP Cylinder SS1
| 31.262 | 7.133 | 2.6629999999999998 | 1.173 | 4.7399999999999998E-2
SS1 | 450 | 365.4 | 332.3 | 263.93 | 191.88 | 122.87 | 49.6
2YT-A1 44.2% 490 psi
YT2-A4 27.9%
401 psi
YT2-A3 31.6% 363 psi
2YT-SS1 20.2% 1,109 psi
Details available in OTC-25994-MS, SPE-180333-MS
Chart: 
| 0.22750000000000001 | 3.7100000000000001E-2 | 3.09E-2 | 6.2199999999999998E-2 | 4.3200000000000002E-2 | 0.19370000000000001 | 2.53E-2 | 0.1227
A4 | 458.18 | 291.22 | 246.25 | 157.88 | 120.47 | 81.44 | 53.37 | 20.22

## Slide 34: Field Collection #3
Details available in SPE-180337-MS, SPE-180278-MS

## Slide 35: FINDINGS – Field Collection #3
YT3-A1 8.3% 505 psi
YT3-A3 39.1% 505 psi
YT3-A2 19.99% 505 psi
YT3-A4 30.7% 495 psi
Reconstructed medical CT images,
False color montage of 6 cross sections X-Z plane
Details available in SPE-180337-MS, SPE-180278-MS
Low High
CT Attenuation
Notes: The advantage in using bottled N2 was the ability to mix and pump at lower rates while maintaining an accurate nitrogen delivery, thus allowing collection of low quality foamed cement samples

## Slide 36: FINDINGS – Field Collection #3
Chart: Porosity of CP Cylinder A1
| 26.56 | 29.226999999999997 | 30.164669999999997 | 29.335000000000001 | 29.589670000000002 | 30.122670000000003 | 29.687329999999999 | 30.248999999999999 | 16.4267
Hal-A1 Porosity | 513.63 | 443.67 | 386.845 | 343.1075 | 276.4975 | 231.5075 | 204.455 | 125.4775 | 49.195
Chart: Permeability of CP Cylinder A1
| 6.4000000000000001E-2 | 8.0399999999999999E-2 | 5.4899999999999997E-2 | 7.6999999999999999E-2 | 0.1179 | 0.15820000000000001 | 0.1363 | 5.1700000000000003E-2 | 0.39939999999999998
Hal-A1-Permeability | 513.63 | 443.67 | 386.845 | 343.1075 | 276.4975 | 231.5075 | 204.455 | 125.4775 | 49.195
Chart: Porosity of CP Cylinder A2
| 37 | 37.35 | 38.049999999999997 | 38.11 | 38.57 | 38.130000000000003 | 37.479999999999997 | 38.07 | 37.96 | 40.19
Hal-A2 Porosity | 482.995 | 446.67 | 417.055 | 363.55 | 304.915 | 267.135 | 236.555 | 187.39 | 101.11 | 66.7
Chart: Permeability of CP Cylinder A2
| 4.0399999999999998E-2 | 2.86E-2 | 3.5000000000000003E-2 | 0.1452 | 0.3458 | 0.14860000000000001 | 7.4800000000000005E-2 | 8.9200000000000002E-2 | 0.3468 | 0.99280000000000002
Hal-A2-Permeability | 482.995 | 446.67 | 417.055 | 363.55 | 304.915 | 267.135 | 236.555 | 187.39 | 101.11 | 66.7
Chart: Porosity of CP Cylinder A3
| 51.526666666666664 | 51.93533333333334 | 51.822333333333326 | 51.928666666666665 | 50.984999999999992
Hal-A3 Porosity | 483.01 | 465.67 | 430.91 | 366.27 | 319.955 | 298.79 | 264 | 205.315 | 149.75 | 117.715 | 68.295 | 16.055
Chart: Permeability of CP Cylinder A3
| 1.21 | 0.9254 | 1.1296999999999999 | 0.87019999999999997 | 0.66920000000000002
Hal-A3-Permeability | 483.01 | 465.67 | 430.91 | 366.27 | 319.955 | 298.79 | 264 | 205.315 | 149.75 | 117.715 | 68.295 | 16.055
Chart: Porosity of CP Cylinder A4
| 43.853000000000002 | 44.835333333333331 | 44.81633333333334 | 44.560750000000006 | 44.895333333333326 | 44.482333333333337 | 44.899000000000001 | 43.064 | 49.575333333333333 | 44.905333333333338 | 46.068999999999996 | 46.31966666666667 | 44.853999999999992 | 45.582999999999998 | 46.419333333333327 | 50.204333333333331
Hal-A4-Porosity | 405.81 | 384.575 | 365.59 | 344.5875 | 321.4975 | 294.49 | 235.36 | 222.47 | 202.33 | 177.94 | 157.875 | 130.57 | 100.9 | 73.165 | 42.86 | 14.21
Chart: Permeability of CP Cylinder A4
| 4.7199999999999999E-2 | 5.74E-2 | 7.0400000000000004E-2 | 7.3300000000000004E-2 | 6.0100000000000001E-2 | 5.8599999999999999E-2 | 8.0699999999999994E-2 | 5.9700000000000003E-2 | 8.4199999999999997E-2 | 8.8499999999999995E-2 | 0.23169999999999999 | 0.1268 | 9.4E-2 | 0.1608 | 0.28549999999999998
Hal-A4-Permeability | 405.81 | 384.575 | 365.59 | 344.5875 | 321.4975 | 294.49 | 235.36 | 222.47 | 202.33 | 177.94 | 157.875 | 130.57 | 100.9 | 73.165 | 42.86 | 14.21
Details available in SPE-180337-MS
YT3-A1 8.3% 505 psi
YT3-A3 39.1% 505 psi
YT3-A2 19.99% 505 psi
YT3-A4 30.7% 495 psi

## Slide 37
The porosity of these samples appeared to correlate well with foam quality
The permeability of the field-generated samples were significantly lower than atmospheric-generated foamed cement samples of the same foam quality
Permeability may be impacted by both foam quality and pressure (need more samples to confirm the statistical validity of this)
FC#3 |  |  | Foam Quality |  | Measured | 
Sample | Material | Pressure (psi) | Targeted | Calculated | Porosity (%) | N2 Permeability (mD)
SS1 | SS | 1015 | 20% | 16.3% | 35.7 | 0.04
SS2 | SS | 957 | 30% | 28.5% | 45.2 | 0.09
A3 | Al | 505 | 40% | 39.1% | 51.6 | 0.96
A4 | Al | 495 | 30% | 30.7% | 45.6 | 0.11
A2 | Al | 505 | 20% | 20.0% | 38.1 | 0.22
A1 | Al | 505 | 10% | 8.3% | 27.9 | 0.13
Details available in SPE-170298-MS, SPE-180333-MS, SPE-180337-MS, SPE-180278-MS, OTC-25994-MS

## Slide 38: Summary and Conclusions
Foam cement samples generated with field equipment display better foamed stability and lower permeability compared to samples generated at atmospheric conditions in the laboratory.
This project indicates that industry practices targeting maximum in-situ foam quality appear conservative insofar as the desire of minimizing permeability.
Properly-executed foamed cementing methods examined during this project all provided better material properties than previously thought based on testing of lab-foamed methods

## Slide 39
Laboratory vs Field
Atmospheric-generated Foamed Cement
30% Foam Quality
Permeability ~19 mD
Field-generated Foamed Cement
33.6% Foam Quality (Calculated)
Permeability 0.09 mD
Details available in SPE-170298-MS, SPE-180333-MS, SPE-180337-MS, SPE-180278-MS, OTC-25994-MS

## Slide 40: Research Scope
Lab
Generated atmospheric samples using API RP 10 B-4 procedures
Class H slurry @ 16.5 lb/gal
  2 recipes, 4 foam qualities (entrained gas by volume)
Field
Samples collected at three industry sites using well completion equipment across a range of foam qualities and pressures
Visualization
Multi-scale computed tomography scanning
SEM
Mechanical testing
Porosity, permeability and strength measurements (Young’s Modulus)
Simulation
LAMMPS modeling of discrete air voids + slurry
Data Sets
Analysis